## Slide 1: Magnet/Coil Thesis Code Help Guide
20/06/30
Patrick McDaniel

## Slide 2: General Notes
The README.txt file has some basic info
The different sections of this *.pptx file give an overview of the five examples included with this code

## Slide 3: Magnet Array Optimization/CAD Scripts
Needs stlwrite, Comsol/Matlab live link (See README.txt)
Run the scripts in the order they’re described in these slides
  Many scripts will generate and save files that will be used by subsequent scripts
  You may need to change filenames in some scripts (eg the fmincon optimization solutions by default have a timestamp in the filename)
  However, I have pre-generated most of these files
    Usually you can run the scripts in any order, in case you want to only look at one step of the pipeline
    I have not included pre-generate versions of files larger than ~10MB (this is mentioned where relevant in these slides)
The basic Inventor CAD model of the magnet array former is in ~/InventorFiles/MagnetArray/B0FormerBase_*.ipt
  Used for STL binary operations (see thesis)

## Slide 4: 1: optsetup_190528_v01.m
Calls several functions
  proc_ROImask_190528_v01()
    Load a brain mask file to produce the target ROI (ie target ROI geometry)
    Generate the set of magnet location points (ie magnet geometry)
    Generate the initial guess magnet design (based on Halbach magnets)
    Save result
  Proc_Dmatrix_L{1,3,5}()
    Generates the field computation matrix for multipole components of order {1,3,5}
    Loads the result of proc_ROImask_190528(); saves the resulting matrices
    Generates matrices to compute field in entire ROI volume (used only for generating field plots)
  Proc_Dmatrix_vol_L{1,3,5}()
    Same as Proc_Dmatrix_L{1,3,5}(), but generates matrices to compute the field just on the ROI boundary (faster, used in-optimization)
  proc_A_comp()
    Uses the magnet symmetry indices (generated in proc_ROImask_190528_v01()) to create a compression matrix
    Enables compression of the D-matrices to work with a reduced set of parameters (smaller, faster field computation)
  Gen_rotmat35_190214()
    Generates the 3rd and 5th order unitary permutation matrices for spherical harmonics; needed for multipole field computation

## Slide 5: 2: optrun_jotunn_190528_v03_solload_run{1,2}.m
Runs the actual iterative optimization using the results of optsetup_190528_v01
  Saves the result in ./Mout_tmp_save.mat at each iteration
  Saves the final result in ./optresults/Mout_[timestamp].mat
  *_run1 uses the analytical initial guess from the setup script.
  *_run2 uses and existing solution – multiplied by a scale factor – as the starting guess for the iterative solver
NOTE: you will not be able to run this code without running optsetup_190528_v01 first
  optrun_* needs matrices generated by optsetup_*
  These matrices are not included in the toolbox because some are >1Gb in size

## Slide 6: 3: gen_block_model_example.m
Converts the solution in ./optresults/Mout_[timestamp].mat to a magnet block struct
  The result from the optimization specifies block size and two Euler angles
  The initial setup file specifies block position
  A third file contains manually-specified values for the third Euler angle
    NOTE: these angles were manually-chosen so that the provided solution (in ./optresults/Mout_Run2Example_test.mat) will not have self-intersections. If you use your own design, you will likely need to tweak these angles
    Self-intersections are physically a problem when building the magnet array. They are also a problem when building the Comsol model, since the boundary condition in the intersection volume is not well-defined).
  Saves a Biot-Savart file in ./Bsfiles/

## Slide 7: 4: gen_STL_Blocks_example.m
Converts the magnet spec struct from (3) into STL files
  Generates a file containing just the magnet blocks
  Generates a file of the blocks with a tolerance offset and an extension (to model the insertion of the magnet into the former)
  Generates a file of the thickened blocks, to serve as “coffers” to hold the actual magnets
  See ./InventorFiles for the *.ipt/*.iam files with which to combine these STLs

## Slide 8: 5: Comsol_buildmodel_script_example_200625.m
Converts the magnet block struct from (3) into a Comsol model and simulates it
  Generates “rounded”/”discretized” block set (need to comment out line to actually simulate)
  Saves *.mph file in ./COMSOLfiles
  Saves text-based simulation result file in ./COMSOLfiles/DataFiles
  Needs matlab/COMSOL live link in order to run
  The actual heavy lifting is done by the auxiliary function: Comsol_buildmodel_func_example_200625()
  The Comsol file is included pre-generated in the toolbox; it is ~152 MB
  The simulated data file is also included (~10MB)

## Slide 9: 6: Comsol_datproc_example_200625.m
Processes the simulated comsol data file
  Loads the result from ./COMSOLfiles/Datafiles
  Plots the simulated masked+unmasked field maps; computes performance metrics

## Slide 10: Permanent Shim Optimization/CAD Scripts
Needs stlwrite (See README.txt)
Run the scripts in the order they’re described in these slides
  Many scripts will generate and save files that will be used by subsequent scripts
  You may need to change filenames in some scripts (eg the fmincon optimization solutions by default have a timestamp in the filename)
  However, I have pre-generated most of these files
    Usually you can run the scripts in any order, in case you want to only look at one step of the pipeline
    I have not included pre-generate versions of files larger than ~10MB (this is mentioned where relevant in these slides)
The basic Inventor CAD model of the shim magnet array former is in ~/InventorFiles/PermanentShimArray/ShimFormerBase_*.ipt
  Used for STL binary operations (see thesis)

## Slide 11: 1: ShimPerm_ptsROI_200110_v01.m
Generate ROI points and shim magnet geometry
  Creates magnet locations/angles (uses manually-chosen, hard-coded positions)
  Uses same ROI as original magnet design
  Saves needed parameters in ./precomp/ShimROI_200110_v01.mat

## Slide 12: 2: ShimPerm_genD_200110_v01.m
Generates field computation matrices/loads target field
  Creates dipole matrices for ROI surface field computation (faster, in-optimization) and for ROI volume field computation (slower, only for plotting field map)
  Compressed D-matrices to only compute field component aligned with measured B0
  Loads measured field map from ./precomp/Bxyz_ROI_200110_v01.mat for use as target field; Note: this field map was measured on a physical magnet in lab, and has no relationship to the result HeadOptimizedMagnetArray code
  Saves everything in ./precomp/D1comp_200110_v01.mat

## Slide 13: 3: optrun_jotunn_200110_v05p3_3opts.m
Runs shim optimization
  Uses ga with 3 block options
  Saves working solution at each iteration of optimization in ./Mout_tmp_save.mat
  Saves results from each ga repetition in ./optresults/Mout_*.mat
NOTE: you will not be able to run this code without running ShimPerm_genD_* first
  optrun_* needs matrices generated by ShimPerm_genD_*
  These matrices are not included in the toolbox because some are large in size

## Slide 14: 4: proc_results_200110_v05p3.m
Processes results from shim ga
  Finds best solution from all repetitions of the optimization; plots it
  Converts middle block option into “empty” block (see thesis for info)
  Plots shim blocks as volume mesh
  Saves STLs of shims blocks, with mechanical tolerance, with extension for inserting block
  Saves BS file of shim magnets (for Biot-Savart program)
    Saves: ./Bsfiles/BSmodel_Shim_Raw_200626.biot -> unmodified result from optimization
    Saves: ./Bsfiles/Bsmodel_Shim_NoZero_200626.biot -> processed to remove zero-volume blocks; convert “middle size” blocks to “empty blocks” (see thesis). Use this *.biot file for simulation.

## Slide 15: Gradient Coil Optimization/CAD Scripts
Needs Yalmip, regu, coildesign_master, and sphericalharmonics toolboxes (See README.txt)
Three sets of scripts, for x, y, and z coils (will only provide instructions for Gx coil in these slides; things are the same for the other two coils)
The scripts are written to be run in the order described by the slides
  Many scripts will generate and save files that will be used by subsequent scripts
  However, I have pre-generated all these files (for the Gradient coil examples)
    Thus, you can actually run these scripts in any order that you want, in case you’re most interested in a particular part of the processing pipeline.
The basic Inventor CAD models of the Gradient coil former are in ~/InventorFiles/GradientCoils/GradFormerBase_*.ipt (the main section) and ~/InventorFiles/GradientCoils/GxFrontplate_base_*.ipt (the front-plate section)
  Used for STL binary operations (see thesis)

## Slide 16: 1: genMesh_Gx_190613_v03.m
Creates the mesh on which to design the Gx coil
  Saves the mesh as a blender *.obj file in: ./mesh/meshGx_Example_200626.obj

## Slide 17: 2: OptSetupGx_190613_v03p2.m
Process the ROI, coil geometry, Optimization settings, etc
  Based on example scripts in Gael Bringout’s coil design toolbox
  Loads mesh from ./mesh/meshGx_*
  Saves 2 files: (1) OptSetupGx_Example_200626.mat ; (2) coil_OptSetupGx_Example_200626.mat
  Both files are used by the optimization script

## Slide 18: 3: OptRunGx_190613_v03p2.m
Runs the optimization; saves the optimized stream function solution
  Based on scripts in Gael Bringout’s coil design toolbox
  Saves the resulting stream function / geometry info in ./optresults/Gx_coil_red_Example_200626.mat

## Slide 19: 4: procGx_190613_v03p2.m
Turns the optimized stream function into a discrete set of isocontours
  Loads ./optresults/Gx_coil_red_Example_200626.mat
  Upsamples the solution onto a higher-res mesh; projects it onto a flat surface; computes isocontours; projects back onto coil geometry surface
  Plots upsampled stream function, isocontour sets, etc.
  NOTE: this can take some time, and makes some very memory-intensive plots (sorry)
  Saves resulting isocontours in ./optresults/cont_Gx_all_Example_200626.mat
  Saves a *.biot file (for Biot-Savart simulation) in ./Bsfiles/~

## Slide 20: 5: STLgenGx_190616_v05_191008_v04.m
Turns the set of 1D isocontours into 2D+3D STL models of the coil wire windings
  Loads ./ optresults/cont_Gx_all_Example_200626.mat
  Uses info about the mesh geometry to compute tangent + normal vectors to all the isocontours
  Performs decimation, smoothing, etc operations on the isocontours
  Saves a 2D STL model of the windings in ./STL/STL2D/Gx2D_190916_v05_191008_v04.mat
  Saves a 3D STL model of all windings in: ./STL/STL3D/Gx_191008_v05p4_3d.mat
  Saves separate 3D STLs for each individual winding in: ./STL/Gx_sep/~ (This allows you to process the windings separately, and avoids self-intersections as may arise when putting all the windings in a single STL file)

## Slide 21: RF Coil Optimization/CAD Scripts
Needs Yalmip, regu, coildesign_master, and sphericalharmonics toolboxes (See README.txt)
The scripts are written to be run in the order described by the slides
  Many scripts will generate and save files that will be used by subsequent scripts
  However, I have pre-generated all these files (for the RF coil examples)
    Thus, you can actually run these scripts in any order that you want, in case you’re most interested in a particular part of the processing pipeline.
The basic Inventor CAD model of the RF Coil former is in ~/InventorFiles/Rfcoil/Helmet_panel_base_*.ipt (“tiles” for the actual windings)
  Used for STL binary operations (see thesis)
  Also included is: ~/InventorFiles/Rfcoil/Helmet_risertool_derive_*.ipt (the helmet in which the “tiles” get epoxied)
Instructions for how to get started with the RF coil scripts can be found in the README.txt file in ~/ExampleScripts/HeadOptimizedRFCoil/

## Slide 22: 1: genMesh_import_RF_200119_v01.m
Creates the mesh on which to design the RF coil
  Loads the numerically-generated mesh in ./mesh_import/Helmet_v6p1_RFsurfonly_200119_v02_meter_bin.stl
  Combines this mesh with an analytically-generated one to make a new mesh (see thesis)
  Saves the result in: ./mesh/mesh_interp_200119_v01.obj

## Slide 23: 2: RF_y_OptSetup_200119_v05.m
Process the ROI, coil geometry, Optimization settings, etc
  Based on example scripts in Gael Bringout’s coil design toolbox
  Loads mesh from ./mesh/mesh_interp_200119_v01.obj
  Saves 2 files: (1) ./precomp/OptSetupRFLR_Example_200626.mat ; (2) ./precomp/coil_OptSetupRFLR_Example_200626.mat
  Both files are used by the optimization script

## Slide 24: 3: RF_y_OptRun_200119_v05.m
Runs the optimization; saves the optimized stream function solution
  Based on scripts in Gael Bringout’s coil design toolbox
  Saves the resulting stream function / geometry info in ./optresults/coil_red_RFLR_Example_200626.mat

## Slide 25: 4: proc_RF_200119v05_200120_v02.m
Turns the optimized stream function into a discrete set of isocontours
  Loads ./optresults/coil_red_RFLR_Example_200626.mat
  Upsamples the solution onto a higher-res mesh; projects it onto a flat surface; computes isocontours; projects back onto coil geometry surface
  Plots upsampled stream function, isocontour sets, etc.
  Saves resulting isocontours in ./optresults/ccont_xyz_RFLR_Example_200626.mat
  Saves a *.biot file (for Biot-Savart simulation) in ./Bsfiles/~
  Finally, it pushes up the “nose” part of the coil (to make more space for the subject)
    Imports ./STL_import/Helmet_v6p1_nose_v01_200120_meter_bin.stl to get the geometry
    Saves the new contours in: ./optresults/cont_xyz_nose_RFLR_Example_200626.mat

## Slide 26: 5: procRFv05_genSTL_200120_v02.m
Turns the set of 1D isocontours into 2D+3D STL models of the coil wire windings
  Loads ./optresults/cont_xyz_nose_RFLR_Example_200626.mat
  Uses info about the mesh geometry to compute tangent + normal vectors to all the isocontours
  Performs decimation, smoothing, etc operations on the isocontours
  Saves a 2D STL model of the windings in ./STL/RFLR_2D_Example_200626.stl
  Saves a 3D STL model of all windings in: ./STL/RFLR_3D_Example_200626.stl

## Slide 27: RF Coil Optimization/CAD Scripts
Needs Yalmip, regu, coildesign_master, and sphericalharmonics toolboxes (See README.txt)
The scripts are written to be run in the order described by the slides
  Many scripts will generate and save files that will be used by subsequent scripts
  However, I have pre-generated all these files (for the RF coil examples)
    Thus, you can actually run these scripts in any order that you want, in case you’re most interested in a particular part of the processing pipeline.
The basic Inventor CAD model of the RF Coil former is in ~/InventorFiles/Rfcoil/Helmet_panel_base_*.ipt (“tiles” for the actual windings)
  Used for STL binary operations (see thesis)
  Also included is: ~/InventorFiles/Rfcoil/Helmet_risertool_derive_*.ipt (the helmet in which the “tiles” get epoxied)

## Slide 28: 1: Block_mur_190311_matlab_Mz.m
Simulates 21 block sizes (all 1”x[y]x1”) in Comsol and saves the resulting magnetization maps
  Saves M-maps in: ./Data/Block_y_*.txt
  Will take time to run; will generate 21x large data files
  Even though this looks like a function, you can run it like a script

## Slide 29: 2: procComsol_all_1090311_Mz.m
Processes the simulation results from Block_mur_*.m and computes multipole coefficients
  Plots the resulting multipole coefficients vs. y-dimension of the block
  Saves the coefficients in: ./matfiles_new/coefs_Mx_mur1p05_190311_test.mat

## Slide 30: 3: procAnal_all_190311_Mz.m
Compares the numerical multipole terms to the analytical multipole terms for a uniformly-magnetized cube. Saves the poly-fit coefficients for the difference
  Loads ./matfiles_new/coeffs_Mz_mur1p05_190311.mat (the multipole terms from the previous step)
  Plots them vs. the computed ideal block analytical solution
  Performs 5th-order polynomial fits to the numerical-analytical difference
  Saves the resulting error terms in ./matfiles_new/pf_*.mat
    NOTE: the files in ./matfiles/* are used by the magnet block array optimization; I recommend you not mess with those files!